Assignment – 1
Programming of Super Computers

1. Execution Environment:

In this assignment the basic usage of papi libraries has been achieved. These libraries allow the access to the hardware counters of the system in a runtime environment.
On Supermuc, we understand that the job must be submitted to a queue, where it allocates the job to the complete node, when the node is free.

We have accessed the hardware info of the cpu but the results in the interactive job mode is different from the job submit mode.

Cpu info	Interactive job	Job cmd file ( llsubmit )
No. of sockets in a node	2	4
No. of cores in a socket	8	10
Multithreads in a core	2	2
Cpu's in a socket	16	20
Total cpu's in a node	32	80

In the above table, the sockets in the nodes were given as zero, but from the other values, we have identified them to the values above. So, the load leveler has allocated extra processing units for the job.

2. Calculation of the metrics:

Through papi libraries the following counters have been accessed.
PAPI_L2_TCM – The total level 2 cache misses.
PAPI_L2_TCA – The total level 2 cache accesses.
PAPI_L3_TCM – The total level 3 cache misses.
PAPI_L3_TCA – The total level 3 cache accesses.

These counters have been estimated for each of the phases described in the source code.

Hence, the cache miss rate

L2_cache_miss_rate = ( PAPI_L2_TCM/PAPI_L2_TCA) * 100;
L3_cache_miss_rate = ( PAPI_L3_TCM/PAPI_L3_TCA) * 100;

Through papi_timers, the time of execution of each phase has been calculated using the calling routine PAPI_get_real_usec(). The execution time has been calculated in micro seconds. And with another counter “PAPI_FP_OPS” the total floating point operations have been counted.

Hence, mflops = Total floating point operations / Ececution time in microseconds.

3. Comparison with ideal performance of the Supermuc:

The peak performance of the supermuc is given by 3 peta flops.
The max we achieved in our case, is given by ….........

The max performance can never be achieved, since there are always latencies in the system. But through a perfect optimization and good data distribution, ideally a good 60-70 % of the peak performance will be achieved.

4. Discussion on the measured data:

5. Text vs binary files:

Generally speaking both the binary and ASCII (text) files are both the same. But the ASCII file stores a byte in terms of an ASCII code, which is actually read as a 1's and 0's by the processor. But the binary file can give you the direct access to the number at the file stream, in terms of number of bytes of data you are expecting the value to store. Hence, ASCII has some kind of inherent little overhead, but both files are regularly used.

Performance Estimation – As expected, reading a binary files which has direct access to the value in terms of bytes si much faster than the ASCII text files. In the data sheet, we can see that the size of the binary file is (1/3) of the size of the text files. Sometimes there is a wastage of space in ASCII files vowing to the fact that it requires 7 bits to represent each character and on overall consuming more space on the system.